## Slide 1: Amateur Radio for Emergency Managers
Santa Clara County ARES/RACES
Michael Fox, N6MEF, RACES Chief Radio Officer
Revised: 11-Mar-2019

## Slide 2: Amateur Radio in Santa Clara County
Santa Clara County
  ~1.8M people
  ~ 8,000 amateur radio licenses
  Many “eyes and ears”
  Most people know someone who is an amateur radio operator
SCCo ARES/RACES
  A group within amateur radio focused on emergency comms systems, procedures, equipment
  About 350 weekly check-ins
  Weekly nets, monthly classes, quarterly drills, public service

## Slide 3: EOC Operations
#1 disaster response issue:
  Poor communications
A key role & responsibility of an Emergency Operations Center is:
  Information Collection, Evaluation, Dissemination

## Slide 4: Amateur Radio in EOC Operations
Amateur Radio can help:
Communications
  Create the capability where it don’t normally exist
  Provide backup capability where existing systems have failed
Information collection and dissemination

## Slide 5: The Standardized Emergency Management System (SEMS)
State
Region
Operational Area
Local Government
Field
Neighborhoods
Shelters
Schools
Hospitals
Unincorporated
Regional EOC
State EOC
County EOC
City EOC
DOCs
DOCs

## Slide 6: How We Think of Communications
Follows the SEMS / NIMS model
Assumptions
  Connectivity will be there when needed
  Communications systems and services (voice, data, video, …) will be there when needed
DOC
Local EOC
Field
OA EOC
Region/State EOC

## Slide 7: Reality Is More Complicated
DOC
Local EOC
Field
OA EOC
Region/State EOC
Connectivity (Land Lines, Mobile, Cable, WiFi, …)
E-mail
Services:
Files
WebEOC
Other
Phone
Redundant Broadband
Broadband
Possibly limited bandwidth
Perhaps little or no connectivity

## Slide 8: Possible Connectivity Problems
DOC
Local EOC
Field
OA EOC
Region/State EOC
Connectivity (Land Lines, Mobile, Cable, WiFi, …)
Files
E-mail
WebEOC
Services:
Other
Phone
Redundant Broadband
Broadband
Possibly limited bandwidth
Perhaps little or no connectivity
Connectivity may not be available at some locations
      Ex: Parks and other field locations
Connectivity can fail at any time, even without a local disaster
    Ex: Equipment, human error, hacking, terrorism, …

## Slide 9: Possible Service Problems
DOC
Local EOC
Field
OA EOC
Region/State EOC
Connectivity (Land Lines, Mobile, Cable, WiFi, …)
Files
E-mail
WebEOC
Services:
Other
Phone
Redundant Broadband
Broadband
Possibly limited bandwidth
Perhaps little or no connectivity
Connectivity at the service provider can fail
Systems that provide the services can fail
May have nothing to do with our own local situation
  Ex: Equipment, human error, hacking, terrorism, …

## Slide 10: Amateur Radio Can Help
When communications at a field site doesn’t normally exist …
Or, when existing systems are degraded or disabled …
Amateur radio doesn’t replace these systems
But it can help fill in some of the gaps
DOC
Local EOC
Field
OA EOC
Region/State EOC

## Slide 11: Amateur Radio Provides Voice AND Data Communications
When most people think of “amateur radio”, they think of voice communications …
Today, we use a mixture of voice and data communications …
In Santa Clara County, we leverage data communications for increased speed, accuracy and alignment with served agency needs

## Slide 12: “When All Else Fails”
2016 Loma Fire
  Commercial power failed
  Generator at radio site failed
  Roads closed; no access to bring backup generator
  Internet service provider networks failed
  Most private communications systems failed
Santa Clara County ARES/RACES network continued to run
  Provided temp, humidity, smoke sensor info to other site tenants
  Used to send/receive Internet email while ISP networks were down
Source: NBC
Crystal Peak – North Tower

## Slide 13: 2017 Wine Country Fires
Mendocino:
Fire destroyed AT&T cable between Ukiah and Willits
Loss of E-911, cellular, landline, cable and most broadband services
Cash only; no ATM machines, credit card readers, …
Sheriff Allman: relying on amateur radio for hospital communications
In Napa and Sonoma:
Electrical service cut off during initial wind storm
Widespread loss of cell service and other communications
Loss of communications at hospitals, shelters, …
Amateur Radio Response:
Local radio amateurs deployed to EOCs, medical centers, nursing homes, Red Cross shelters, high schools, …
Coordinated delivery of food, bedding, shelter supplies, donations

## Slide 14: Amateur Radio in EOC Operations
Amateur Radio can help:
Communications
  Create the capability where it don’t normally exist
  Provide backup capability where existing systems have failed
Information collection and dissemination

## Slide 15: Information Collection
Information needs to be collected from places that lack communications
Amateur Radio
Can provide communications at schools, shelters, hospitals, neighborhoods and for groups such as CERT, Red Cross, CADRE, and others.
Report on situation, collect status, make requests
DOC
EOC
Field

## Slide 16: Example: Earthquake Damage Reports

## Slide 17: Earthquake Damage Reports
DOC
EOC
Santa Clara County amateur radio operators are trained how to send in damage reports using the Modified Mercalli Scale
Quickly establishes a county-wide picture of where and how much damage has occurred

## Slide 18: Example: Schools / Local EOC

## Slide 19: Example: Schools / Local EOC
Schools report to school district; school districts report to city EOC
  Status (damage, injuries, …), resource requests, H&W
Amateur Radio:
  School districts to city EOC (primary or backup)
  Schools to school districts (backup)
Amateur Radio Operator
EOC
Schools
School District
Office(s)
School
District
Operator
Amateur Radio
Operator
Business
Radio
Amateur
Radio

## Slide 20: Example: Neighborhoods / Local EOC
Mountain View CERT and ARES/RACES (Amateur Radio)

## Slide 21: Example: Neighborhoods / Local EOC
Community Emergency Response Teams report to neighborhood command posts; CP reports to city EOC
  Damage assessment
Amateur Radio: neighborhood CP to EOC
Amateur Radio
Operator
EOC
CERT
Teams
Neighborhood Incident Command Posts
CERT
Operator
Amateur Radio
Operator
FRS or MURS
Radio
Amateur
Radio

## Slide 22: CERT Collects Neighborhood Data

## Slide 23: Summary Data Ready to Transmit

## Slide 24: Summary Displayed in Mountain View EOC

## Slide 25: Example: Hospitals, Allied Health
Various health-specific forms or other messages

## Slide 26: Example: Hospitals, Allied Health
Medical info is reported to MHJOC; municipal issues are reported to the city EOC; OA EOC supports both
  Bed status, facility status, resource requests, municipal issues
Amateur Radio:
  Hospital to (MHJOC or City EOC) to OA EOC
  Support for Allied Health facilities is new
Hospital
Medical Health
Joint Operation Center
OA EOC
Allied Health
City EOC
Amateur Radio
Operator
Amateur Radio Operator
Amateur Radio
Amateur Radio
Amateur Radio Operator

## Slide 27: Example: City EOC / County EOC
EOC 213RR Resource Request or other messages

## Slide 28: Example: City EOC / County EOC
City EOC
OA EOC
Deliver
Fill Out Paper Form
Give to
amateur
radio
operator
Scenario:
City EOC needs to send a Resource Request form to the County EOC
Connectivity to WebEOC not available at one or both ends
Transmit via radio from anywhere in the county
City EOC radio operator sends form
County EOC radio operator receives form
Print Form

## Slide 29: Example: Alternate 911
Under development for: Cupertino, Los Altos Hills, Saratoga

## Slide 30: Alternate 911
DOC
EOC
Dispatch
Law,
Fire,
EMS
Issues
Local Gov
Issues
Fire Station or Ark Location
Amateur
Radio
Equipped and Staffed

## Slide 31: Information Dissemination
After analysis, synthesis, information can be distributed to field resources and the public
Amateur Radio
Can be used to distribute information to schools, shelters, hospitals and groups such as CERT, Red Cross, CADRE, and others.
Press releases and public service announcements can distributed to the general public
DOC
EOC
Field

## Slide 32: Example: Disseminating info to field responders

## Slide 33: Information Dissemination: Field
Situational awareness, common operating picture, resource status, prioritization, analysis, support, …
Amateur radio: each SEMS level
Field
DOC
City EOC
County EOC
Amateur radio operators are trained in message passing techniques (voice and data) which help deliver the message correctly and quickly

## Slide 34: Example: Distributing Information to the Public

## Slide 35: Distributing Public Info
Schools
Shelters
Neighborhoods
… wherever needed
Amateur
Radio
Broadcast
Media
Social
Media
What about those who don’t have access or where communications systems are damaged?
PIO

## Slide 36: Example: Beyond the Op Area

## Slide 37: Example: Beyond the Op Area
Communications outside of our operational area is also important
  Who
    Other Operational Areas
    Region and State
    Elsewhere
  Why
    Situational awareness
    Common operating picture
    Resource sharing
    Coordination
    …
Amateur radio can compliment existing communications paths or act as backup during failures
Santa Clara Co EOC
Other OA EOC(s)
Region/State EOC

## Slide 38: EOC Readiness: Amateur Radio
Two related but separate questions:
Is your EOC ready for Amateur Radio?
Is Amateur Radio ready at your EOC?

## Slide 39: Readiness Assessment
Each city/OA has a Chief Radio Officer
  Manages amateur radio emergency comms efforts
  Best single point of contact for EOC staff
Equipment & facilities
  Do sufficient radios, antennas, computers, etc. exist for simultaneous operations on standard nets?
  Do you have sufficient space allocated? Accessible to/from EOC?
  We have standardized recommendations for city EOCs, hospitals, …
Personnel
  Do you have a sufficient number of amateur radio operators and are they sufficiently trained?
  Are you helping to recruit, encouraging participation, training?
  We have a comprehensive training and credentialing program
Procedures
  Do you have EOC procedures for utilizing amateur radio?
  Do your training, documentation, exercises include amateur radio?

## Slide 40: Summary
Amateur radio can help at the EOC with
  Information collection and dissemination
  Communications
    Where it doesn’t normally exist
    Backup where existing systems are degraded or failed
Amateur radio in Santa Clara County
  Standards for people, procedures, equipment
  Robust and active training and exercise schedule
    Weekly nets, monthly classes, quarterly drills
    Public service events (races, parades, …)
  Each jurisdiction should assess readiness, encourage participation
For more information:
  https://www.scc-ares-races.org